## Slide 1
GROUND SLOW, MOVE FAST
DualVLN
A Dual-System Foundation Model for Generalizable Vision-and-Language Navigation
What it is, how it works, and how it compares with StreamVLN
Wei, Wan, Peng, Yu, Yang, Feng, Cai, Zhu, Wang, Pang, Liu · arXiv:2512.08186 · December 2025
Checkpoint: InternRobotics/InternVLA-N1-DualVLN · Code: InternRobotics/InternNav

## Slide 2
AGENDA
What this talk covers
▍ 1 Background VLN-CE, the task and its metrics
▍ 2 The problem why end-to-end VLM → discrete action hurts
▍ 3 DualVLN System 2, System 1, and latent plans
▍ 4 Results R2R / RxR Val-Unseen against prior work
▍ 5 StreamVLN slow-fast context, the model we run today
▍ 6 Head-to-head architecture, output, sensing, latency
▍ 7 Our stack one HTTP contract, one trajectory follower
▍ 8 Benchmark the controlled A/B we can now run in Isaac
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
2

## Slide 3
BACKGROUND
Vision-and-Language Navigation in continuous environments
The task
Give a robot one free-form sentence — "walk past the reception desk and stop at the second door" — and it must reach the described goal in an environment it has never seen, using only its own camera stream.
VLN-CE replaces the old navigation-graph teleports with continuous control, so the agent has to actually drive: no oracle waypoints, no map, no pre-built topology.
THE FOUR METRICS ON EVERY SLIDE
NE Navigation Error — metres from the goal at stop. Lower is better.
OS Oracle Success — did the path ever pass within 3 m of the goal.
SR Success Rate — stopped within 3 m of the goal.
SPL Success weighted by Path Length — SR penalised for detours.
nDTW Path fidelity against the reference route (RxR).
Benchmarks: R2R-CE short, terse English instructions · RxR-CE long, multilingual, fine-grained instructions — the harder, more path-faithful split
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
3

## Slide 4
THE PROBLEM
Why one network mapping pixels → discrete actions falls short
RGB frame
7B Vision-Language Model
FORWARD 0.25 m / TURN 15°
▍ The VLM sits in the control loop. Every motion needs another billion-parameter forward pass, so the robot moves at the speed of the language model.
▍ Motion is quantised. A 0.25 m / 15° vocabulary cannot express a smooth arc; the robot stutters through stop-start bursts.
▍ Reasoning horizon is short. Predicting the next few actions is not the same as committing to a plan, so long instructions drift.
▍ No room to react. Between two VLM calls nothing is watching the world — a person stepping in front of the robot is seen late.
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
4

## Slide 5
THE PAPER
Ground Slow, Move Fast
A Dual-System Foundation Model for Generalizable Vision-and-Language Navigation
ARXIV
2512.08186 · 9 December 2025
AUTHORS
Meng Wei, Chenyang Wan, Jiaqi Peng, Xiqian Yu, Yuqiang Yang, Delin Feng, Wenzhe Cai, Chenming Zhu, Tai Wang, Jiangmiao Pang, Xihui Liu
MODEL
InternVLA-N1-DualVLN · 8B params · BF16
LICENCE
CC BY-NC-SA 4.0 (non-commercial)
CODE
github.com/InternRobotics/InternNav
Positioned as the dual-system release of the InternVLA-N1 navigation foundation model line.

## Slide 6
DUALVLN ARCHITECTURE
Two systems, running at two different speeds
SYSTEM 2 “ground slow” ~2 Hz
VLM global planner
Qwen2.5-VL (7B), fully fine-tuned.
Reads the instruction and the current image and grounds the next sub-goal as a pixel goal — a point in the image — then emits a latent plan for System 1.
≈ 0.7 s per trajectory-token inference with KV-cache reuse
SYSTEM 1 “move fast” ~30 Hz
Diffusion Transformer policy
384 hidden dim · 12 layers · 6 heads · DepthAnythingV2-Small ViT encoder.
Conditioned on the pixel goal and System 2's latent features, it outputs a short continuous trajectory rather than a discrete action.
32 trajectories in 0.03 s in parallel with TensorRT
Asynchronous by design. System 1 keeps driving while System 2 is still thinking — the robot never waits for the language model.
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
6

## Slide 7
WHAT IS NEW
The key idea: latent plans instead of an explicit pixel goal
A pixel goal is ambiguous
"Go to that doorway" pinned to one image coordinate loses everything the planner knew but could not draw: which side to pass on, how far past it to stop, what the instruction said next.
A latent plan keeps it
System 2 hands System 1 a learned latent vector as well. It is a richer intermediate representation than a point, and it is trained end-to-end with the controller that consumes it.
TWO-STAGE CURRICULUM TRAINING
Stage 1 Pre-train both systems separately, supervised by / conditioned on explicit pixel goals.
Stage 2 Freeze System 2. Fine-tune the newly added latent plans jointly with System 1, asynchronously and end-to-end.
Result faster convergence and better end-to-end performance than the earlier explicit-goal InternVLA-N1 variants.
Read it as: the VLM stops being a controller and becomes a planner; a small fast policy becomes the controller.
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
7

## Slide 8
RESULTS · R2R
DualVLN leads every VLN-CE metric it reports
+7.4 SR and +6.6 SPL over StreamVLN on R2R Val-Unseen, and it beats NaVILA, Uni-NaVid and NaVid by a wider margin still.
All numbers as reported in the DualVLN paper's comparison table (arXiv 2512.08186). StreamVLN's own paper reports 56.4 SR / 50.2 SPL for its released checkpoint and 56.9 / 51.9 as its headline.
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
8

## Slide 9
RESULTS · RXR
The gap widens on the harder, path-faithful split
+8.5 SR, +5.8 SPL, +8.1 nDTW over StreamVLN on RxR Val-Unseen. The nDTW jump matters most: it says DualVLN follows the described route, not just that it arrives.
Navigation error falls from 6.22 m to 4.58 m — the continuous controller stops closer to where the instruction actually pointed.
DualVLN · Ground Slow, Move Fast (arXiv 2512.08186)
9

## Slide 10
THE BASELINE
StreamVLN — the model we are running today
Streaming VLN via slow-fast context modelling
arXiv:2507.05240 · ICRA 2026 · InternRobotics — the same lab that released DualVLN.
StreamVLN attacks the same latency problem, but from the context side rather than the architecture side: keep one VLM, make its history cheap enough to run in real time.
HOW IT KEEPS UP
Fast dialogue context sliding window of 8 multi-turn dialogues drives responsive action generation.
Slow memory context 8 × 196 tokens of compressed history, pruned with a 3D-aware voxel strategy (−28 % to −32 % tokens).
KV-cache reuse over 99 % of prefill time removed; context size and cost stay bounded on long streams.
Backbone LLaVA-Video 7B / Qwen2-7B Output 4 discrete actions per call Latency 0.27 s per call Training 1 500 A100-hours
StreamVLN · SlowFast Context Modeling (arXiv 2507.05240)
10

## Slide 11
COMPARISON
Head-to-head
 | DualVLN | StreamVLN
Core idea | Split planning from control: two systems, two rates | Keep one VLM, make its context cheap
System 2 / backbone | Qwen2.5-VL 7B pixel-goal planner | LLaVA-Video 7B (Qwen2-7B)
System 1 / controller | Diffusion Transformer, 384-d, 12 layers | — none, the VLM is the controller
Model output | Continuous trajectory (waypoints) | 4 discrete actions (0.25 m / 15°)
Interface | Latent plan + pixel goal | Autoregressive action tokens
Planner rate | ≈ 2 Hz (0.7 s) | ≈ 3.7 Hz (0.27 s per 4 actions)
Control rate | ≈ 30 Hz (0.03 s for 32 trajectories) | Tied to the VLM call
Reacts mid-plan? | Yes — System 1 replans continuously | Only at the next VLM call
R2R Val-Unseen SR / SPL | 64.3 / 58.5 | 56.9 / 51.9
RxR Val-Unseen SR / SPL | 61.4 / 51.8 | 52.9 / 46.0
Rates are the figures each paper reports for its own deployment; they are not measured on the same hardware.
Comparison · DualVLN vs StreamVLN
11

## Slide 12
OUTPUT & CONTROL
The difference that matters for a real robot
StreamVLN
FORWARD
FORWARD
TURN 15°
FORWARD
one call → 4 quantised steps
DualVLN
one call → a continuous path
▍ Smoothness. A trajectory can be tracked by a normal velocity controller; an action list cannot be, without stop-start motion.
▍ Reactivity. System 1 re-emits a path ~30× per second, so an obstacle appearing mid-plan is handled before the planner even notices it.
Comparison · DualVLN vs StreamVLN
12

## Slide 13
BEFORE YOU SWITCH
Sensing, licensing, and the practical caveats
 | DualVLN | StreamVLN
Policy input (paper) | RGB — model card states depth not required | RGB stream
Released deployment code | Takes paired RGB + metric depth + intrinsics; System 1 consumes depth | RGB JPEG only
Licence | CC BY-NC-SA 4.0 — non-commercial | See StreamVLN repo
Model size | 8B (7B VLM + small DiT) | 7B
Real-robot platforms | Turtlebot4, Unitree Go2, Unitree G1 | Unitree Go2
Extra evaluation | Human Collision Rate for dynamic/social scenes | Hallway / bedroom / office scenarios
Watch this one. The paper headlines RGB-only, but the published real-world agent feeds depth into System 1. Our integration therefore sends synchronised depth + intrinsics to DualVLN and records the sensor difference in the benchmark metadata.
Comparison · DualVLN vs StreamVLN
13

## Slide 14
INTEGRATION
Both models behind one interface in our stack
Isaac Sim · Stretch 3
/rgb /depth /camera_info /odom → /cmd_vel
vln_agent_node (ROS 2, model-free)
Shared HTTP client (protocol v2) Shared trajectory follower — 20 Hz, 0.25 m/s, 0.5 rad/s Identical limits for both models
Remote GPU servers
StreamVLN :18080
DualVLN :18082
SWITCHING IS ONE ARGUMENT
./run_vln_demo.sh backend:=streamvln
./run_vln_demo.sh backend:=dualvln
▍ No model code in any ROS image. Inference stays in two ROS-free GPU containers; the robot side is an HTTP client plus a controller.
▍ StreamVLN actions become waypoints. Its 0.25 m / 15° steps convert losslessly into the same trajectory the follower runs for DualVLN — so the controller is never the variable under test.
Integration · stretch_main / vln_policy
14

## Slide 15
BENCHMARK
The controlled A/B we can now run
▍ Same prompt, verified. Prompt hashes must match across both models or the run is rejected.
▍ Same reset. Isaac /set_entity_state teleport, then five consecutive odometry samples within 5 cm / 3° before the clock starts.
▍ Same controller. 20 Hz, 0.25 m/s, 0.5 rad/s, 0.35 m lookahead — identical for both backends.
▍ Order alternated. Reps 1/3/5 StreamVLN first; reps 2/4 DualVLN first, so warm-up drift cannot favour either.
WHAT EVERY TRIAL RECORDS
SPL @ 1 m and 3 m success only if the model itself stops in radius
Executed path integrated from raw odometry after reset
Shortest path from a verified reference polyline, never straight-line distance
Rate breakdown camera Hz, model updates/s, client Hz, server FPS, System 1 / System 2 FPS, controller Hz
Per-step JSONL one row per /step with poses, output and timings
Still to do: measure and verify the real hospital-scene start poses, goals and reference polylines — the manifest currently holds a placeholder route.
Benchmark · stretch_main / vln_policy
15

## Slide 16
TAKEAWAYS
What to remember
1
DualVLN separates thinking from driving. A 7B VLM plans at ~2 Hz; a small diffusion policy drives at ~30 Hz. The robot stops waiting for the language model.
2
Latent plans are the contribution. A learned vector carries more of the planner's intent than a single pixel goal, and it is trained jointly with the controller that uses it.
3
It wins on every reported metric. +7.4 SR on R2R and +8.5 SR on RxR over StreamVLN, with a large nDTW gain — it follows the route, not just the destination.
4
StreamVLN is still the simpler system. One model, one context, RGB only, permissively usable. DualVLN is 8B, CC BY-NC-SA, and its deployment path wants depth.
5
We can now settle it empirically. Same prompt, same reset, same controller, five repetitions per route — on our own robot in our own scene.

## Slide 17
SOURCES
References
▍ Ground Slow, Move Fast: A Dual-System Foundation Model for Generalizable Vision-and-Language Navigation
Wei et al., arXiv:2512.08186, December 2025 · arxiv.org/abs/2512.08186
▍ StreamVLN: Streaming Vision-and-Language Navigation via SlowFast Context Modeling
arXiv:2507.05240, ICRA 2026 · arxiv.org/abs/2507.05240
▍ InternVLA-N1-DualVLN checkpoint
huggingface.co/InternRobotics/InternVLA-N1-DualVLN · CC BY-NC-SA 4.0
▍ InternNav — inference code, evaluation protocol, Gradio demo
github.com/InternRobotics/InternNav · pinned at 7a5c624
▍ StreamVLN implementation
github.com/InternRobotics/StreamVLN
▍ Isaac Sim ROS 2 simulation control (/set_entity_state)
docs.isaacsim.omniverse.nvidia.com · 5.1.0 ros2_tutorials
References
17